## Slide 1: CloudNaaS: A Cloud Networking Platform for Enterprise Applications
Theophilus Benson*, Aditya Akella*, Anees Shaikh+, Sambit Sahu+
(*University of Wisconsin, + IBM Research)

## Slide 2: Current Cloud Offerings
introduction of cloud networking functions
Limited control of the network
  Requires integration of third-party solutions
  Limits the opportunity to migrate production applications
Examples of Missing Features
No ability to create VLANs in the cloud
No facility to manage bandwidth or QoS
Limited ability to craft network segments
No intelligence for dynamically structured networks
persistent connectivity for services e.g., “elastic IP”
base IP connectivity
VPN to the enterprise e.g., “Virt Private Cloud”
Network monitoring e.g., “CloudWatch”
Server load balancing e.g., “Elastic Load Balancing”
Third-party
virtual appliances
reference: http://broadcast.oreilly.com/2010/12/ cloud-2011-the-year-of-the-network-in-the-cloud.html

Subnets and ACLs e.g., “VPC” enhancements

## Slide 3: Contributions
Design and implementation of CloudNaaS
  Enforce enterprise policies
  Fine-grained control over network
Optimizations to improve scalability
  Overcome hardware limitations
Prototyped and evaluated
  Different workloads and topologies

## Slide 4: Design Challenges
Operate within physical limitations
  Limited network bandwidth
  Limited network state (switch memory)
Operate efficiently at large scale
  Compute , install, and teardown virtual networks
  Recovering virtual network when failures occur

## Slide 5: Cloud Networking-as-a-Service
Cloud controller
  Provides base IaaS service for managing VM instances and images
  Self-service provisioning UI
  Connects VMs via host virtual switches
Network controller
  Provides VM placement directives to cloud controller
  Generates virtual network between VMs
  Configures physical and virtual switches
virtual network
OS
middleware
application
VM
Network specification
OS
middleware
application
VM
OS
middleware
application
VM
Cloud controller
Network controller
self-service UI

## Slide 6: Supported Abstractions
traffic is allowed to flow only over explicitly defined virtual network segments (“default off”)
virtualnet
- segments connect groups of VMs
- associated with network services
EXTERNAL
middlebox
resv bandwidth
VLAN / scoped bcast
…
networkservice
- attach capabilities to a virtualnet
- supports combination of network services

## Slide 7: Using CloudNaaS
Cloud Controller
Physical Host
VM
Network Controller
Virtual
Switch
Programmable
Switch
User enter policies
Comm. Matrix created
N/W forwarding state
VM placement decided
VMs placed
Virtual switch installed
N/W state installed
Notes: Reverse 6/7

## Slide 8: Prototype
Cloud Controller: OpenNebula 1.4
  Modified to accept user-specified network policies
  Modified to accept placement decisions from Network Controller
Network Controller: NOX and OpenFlow-enabled switches
  Network controller implemented as a C++ NOX application (~2500 LOC)
  HP Procurve 5400 switches w/ OpenFlow 1.0 firmware
VM2
VM4
VM1
VM5
VM8
VM3
HOST1
HOST2
HOST3
HOST4
HOST5
Network Controller
OpenNebula
Cloud Controller
SWITCH 1
SWITCH 4
SWITCH 2
SWITCH 3
SWITCH 5

## Slide 9: Evaluations
Driven by experiments and simulations
Topology: Canonical 3-tier tree
Size (largest): 270K VMs, 1000 ToR switches, 30K hosts
Default placement scheme: striping
Workloads
  Interactive N-tier application (e.g. SharePoint/Exchange)
  Batch cluster application (e.g. Hadoop job)

## Slide 10: Results
Speed to compute virtual networks?
  120s for largest data center (worst case)
Speed to recover from host failure?
  0.2s (caching of network state)
Speed to recover from link/device failure?
  2-10s for link failures (0.2s with optimizations)
  Device is an order of magnitude more

## Slide 11: Results
Optimizations allow support of 3X more VNs
  Most savings at the core
VM placement allows even better scaling
  Applications supported: 4X
Algorithms | Virtual switch | ToR | Aggregation | Core | # of Apps
Default Placement | 313 | 13K | 235K | 1068K | 4k
Default placement + Optimizations | 0% | 93% | 95% | 99% | 12.2K
Placement Heuristic + Optimizations | 0% | 99.8% | 99% | 99% | 15.9K

## Slide 12: Summary
CloudNaaS allows enterprises to enforce network policies
  Recreate data-plane in the cloud
Showed effectiveness and robustness
  Increases cloud’s capacity by 4X
  Low overhead for creation or deletion of virtual nets